K E R M I T - 1 1   f o r   R T - 1 1 S J / F B


  S P E C I A L   F L O P P Y - B A S E D   M I N I M U M   V E R S I O N


	     V  0  3 . 6  2 - 5 _ m i n      3 1 - M a y - 9 3


KRTMIN is a special edit of the KRT Kermit-11 package to accommodate small
floppy disk (RX-0*) based systems, and is distinguished by these features:

1.  Extremely small size, only requires 33kb of memory.

2.  Needs no system (Line Time) clock.

3.  Overlays rearranged to minimize thrashing of the floppy disk.

4.  Runs under RT-11 SJ and FB from V4 and up, and probably V3B.

5.  Non-EIS CPUs are supported.

Communication is ONLY VIA THE CONSOLE PORT.  No comm handler support exists
in this version, however the server remains fully functional, including the
ability to do up to 1920 byte packets (best confined to outbound transfers).

In other words, this package is meant to provide a means of extracting files
from hardware where there is no other way to communicate with it besides the
console terminal line.  As such, this special version of Kermit omits PLENTY
of what exists in the KRT release from which this special version was made.

See the full KRT package documentation for detailed info.  Its source files
are fully commented, those supplied here are stripped in order to fit it on
the medium which it supports.

The main differences are in the default file names for the HELP text file
and the init file, and the paths for these and TAKE files:

	KRTHLP.HLP   =   KRTMIN.HLP	! path = SY, DK
	KRT   .INI   =   KRTMIN.INI	! path = DK, SY
	TAKE files			! path = DK, SY
  
To use, edit KRTMIN.INI as required then copy it, KRTMIN.HLP and KRTMIN.SAV
to the destination device of your choice.  The .SAV image may be renamed as
desired however the .HLP and .INI files must not be renamed as KRTMIN calls
them explicitly by name.

If you need to tweak the wait loop so the time_outs are closer to real time
for your particular CPU, see the SUSPEN:: routine in the KRTRMS.MIN module.

        Billy Youdelman                 youdelman@eisner.decus.org
        PO Box 1207                     billy@mix.com
        Culver City, California 90232
        USA



The following files comprise everything required for KRTMIN:

KRTATR.MIN	Attribute packet processing
KRTCDF.MIN	Command macro definition .include file
KRTCMD.MIN	Main program loop, commands calling O:1
KRTCM1.MIN	O:1 overlay for the rest of the commands
KRTCOM.MIN	Main loop commands data table
KRTCVT.MIN	File name conversion routines
KRTDAT.MIN	Global read/write data
KRTDEB.MIN	EXAMINE command, display memory by symbol or address
KRTDEF.MIN	Packet definition .include file
KRTDIR.MIN	Directory operations
KRTDSP.MIN	I/O dispatching
KRTEDI.MIN	SL command line editor
KRTERM.MIN	I/O support for the controlling terminal line (TT)
KRTERR.MIN	Error messages
KRTHLP.MIN	HELP command processor
KRTINI.MIN	Initialization, packet logging
KRTMAC.MIN	Macro definitions .include file
KRTMIN.ASM	Assembles all .MIN (actually .MAC) source modules using KRTNHD
KRTMIN.BAS	Builds KRTHLP.MIN from KRTMIN.PRE + KRTMIN.HLP
KRTMIN.BWR	"Beware" file, known bugs and possible things to come..
KRTMIN.COM	Link command file
KRTMIN.DOC	Release Notes
KRTMIN.HLP	HELP text file
KRTMIN.INI	Sample initialization file
KRTMIN.MAP	Link map of KRTMIN.SAV
KRTMIN.PRE	KRTHLP.MIN sans its RMS index data, which KRTMIN.BAS adds..
KRTMIN.SAV	Special floppy disk based minimum version image of Kermit-11
KRTNHD.MIN	MUL, DIV, SOB, ASH macros for non-EIS CPU
KRTOSI.MIN	One-shot initialization at program start
KRTPAK.MIN	Low level packet processing
KRTREC.MIN	Incoming file protocol processing
KRTRMS.MIN	File access, RMS emulation
KRTSEN.MIN	Outgoing file protocol processing
KRTSER.MIN	Server support
KRTSHO.MIN	SHOW, COPY, DELETE, PRINT, RENAME commands
KRTSJ .MIN	Root module for low memory overlays image
KRTSTD.MIN	SET command data table
KRTST0.MIN	SET command overlay 0
KRTST1.MIN	SET command overlay 1
KRTSUB.MIN	Misc common utility routines
KRTUTL.MIN	Misc utility routines

31-May-93
-eof-